## Slide 1: Challenges for Hydrological Science in Arid and Semi-Arid Regions Howard Wheater, Canada Excellence Research Chair Laureate & Founding Director, Global Institute for Water Security, University of Saskatchewan, Canada; Emeritus Professor of Hydrology, Imperial College London, UK
International Conference on Water Security, June 18 2018

## Slide 2: Motivation
The hot deserts of the world are, by definition, the regions where water is most scarce, yet they face rapid population growth, increasing pressures on water resources, and increasing threats from extreme events.
Appropriate water management is crucial, yet arid regions have special hydrological characteristics and suffer problems of limited data and limited scientific understanding.
Routine use of models for flood design, flood forecasting and water resources management continues to be challenging. Few models are specifically designed for arid areas, and there is limited research to inform model application.
What are the future science and modelling needs and challenges?

## Slide 3
Jebel Al-Hajar
Falaj system – taps shallow ground
water from a wadi channel bed
Northern Oman Flood Study, 1981
Al-Batinah coastal plain

## Slide 4
Some effects of the flood of 3 May 1981
Wadi Adai - The main highway connecting the North and South of Oman
This was a newly- completed embanked road section before the storm

## Slide 5
The search for storm rainfall data
Map of available storm rainfall data
3 May 1981
Rainfall
temporal
profiles

## Slide 6
Table 2.1. Summary of Muscat rainfall data (1893 -1959) (after Wheater and Bell, 1983) |  |  |  |  |  |  |  |  |  |  |  | 
Monthly rainfall (mm) | Jan. | Feb. | Mar. | Apr. | May | June | July | Aug. | Sept. | Oct. | Nov. | Dec.
Mean | 31.2 | 19.1 | 13.1 | 8.0 | 0.38 | 1.31 | 0.96 | 0.45 | 0.0 | 2.32 | 7.15 | 22.0
Standard deviation | 38.9 | 25.1 | 18.9 | 20.3 | 1.42 | 8.28 | 4.93 | 2.09 | 0.0 | 7.62 | 15.1 | 35.1
Max. | 143.0 | 98.6 | 70.4 | 98.3 | 8.89 | 64.0 | 37.1 | 14.7 | 0.0 | 44.5 | 77.2 | 171.2
Mean number of raindays | 2.03 | 1.39 | 1.15 | 0.73 | 0.05 | 0.08 | 0.10 | 0.07 | 0.0 | 0.13 | 0.51 | 1.6
Max. daily fall (mm) | 78.7 | 57.0 | 57.2 | 51.3 | 8.9 | 61.5 | 30.0 | 10.4 | 0.0 | 36.8 | 53.3 | 57.2
Number of years record | 63.0 | 64 | 62 | 63 | 61 | 61 | 60 | 61 | 61 | 60 | 61 | 60
Muscat mean annual rainfall 106mm

## Slide 7
All available sub-daily precip data were analyzed to produce design guidelines and estimate storm frequency

## Slide 8
A simple distributed hydrological model – runoff from overland flow + channel routing
The Wadi Adai flood hydrograph was reconstructed from witness accounts and surveys of high-water trash marks
And then used to define the parameters of a hydrological model for subsequent design application

## Slide 9
A simple distributed hydrological model – runoff from overland flow + channel routing
The Wadi Adai flood hydrograph was reconstructed from witness accounts and surveys of high-water trash marks
And then used to define the parameters of a hydrological model for subsequent design application
This regional flood analysis was used for more than 20 years.
But note two other memorable Oman events:
Masirah Island 1977 - 431 mm in 1 day
Cyclone Gonu 2007 – 960mm reported

## Slide 10: Some Lessons Learnt
It is not uncommon to receive a year’s rainfall in a day – extreme events dominate the water balance and can be highly damaging
Hydrological monitoring is problematic
- spatial rainfall is variable and difficult to capture with conventional gauge networks
- the only flow gauge to observe the 3 May event was washed away and lost without trace
Traditional knowledge can be important - older properties in Muscat had raised entrances; when the streets flowed with water, there was no ingress. New developments had been located in flood-prone areas

## Slide 11
South West Saudi Arabia
Representative Basins study (1983-1988):
Wadis Yiba, Habawnah, Tabalah, Liyyah and Lith
(456 to 4930 km2 in area)
Staffed by a full-time resident team of hydrological technicians in each wadi, networks typically consisted of 20 rain gauges, a WMO climate station, multiple flow gauges, and several alluvial wells.

## Slide 12
South West Saudi Arabia
Asir mountains

## Slide 18
Basin area
3123 km2

## Slide 20
GW level
GW level
GW level
GW level
GW level
Flow
Flow

## Slide 24: Key science issues
The experimental basins were an invaluable contribution to regional knowledge, giving important data and process insights, e.g.:
Spatial variability of precipitation is hard to characterize
Overland flow is a dominant process – but effects of surface processes on infiltration are little studied
Wadi flows are dynamic (and dangerous), reduce with distance downstream, and are unreliable indicators of upstream flows
Transmission losses are dominant – but complex streambed processes are variable in space and time and poorly understood
Groundwater recharge from ephemeral surface flows is a key water resource, yet is uncertain, depending on complex surface processes and heterogeneous subsurface properties

## Slide 25: What about other arid areas?
A critical lack of high-quality observations has been widely recognized for many decades (McMahon, 1979; Nemec and Rodier, 1979; Pilgrim et al., 1988). Sadly those comments can largely be reiterated today.
One important exception is the Walnut Gulch basin, in Arizona, SW USA
And some major projects have spurred extensive studies. Notable examples are the recent dispute between Chile and Bolivia concerning the Silala River, heard before the International Court of Justice, The Hague in 2023, and the safety assessment for a proposed nuclear waste repository at Yucca Mountain, Nevada, USA ($10 billion dollars spent on site investigation, but an inadequate hydrometric network to define rainfall, surface flows and near surface hydrology)
McMahon, T.A., (1979) Hydrological characteristics of arid zones. Proceedings of a Symposium on The Hydrology of Areas of Low Precipitation, Canberra, IAHS Publ. No. 128, pp. 105-123.
Nemec, J. and Rodier, J.A., (1979) Streamflow characteristics in areas of low precipitation. Proceedings of a Symposium on the Hydrology of Areas of Low Precipitation, Canberra, IAHS Publ. No. 128, pp. 125-140
Pilgrim, D.H., Chapman, T.G. and Doran, D.G., (1988) Problems of rainfall-runoff modelling in arid and semi-arid regions. Hydrol. Sci. J., 33(4): 379-400.

## Slide 26
Walnut Gulch, near Tombstone,
Arizona, USA
A US Department of Agriculture experimental basin from 1953-present;
- 88 recording raingauges,
30 instrumented sub-watersheds,
flows monitored by 11 critical depth flumes

## Slide 27: USDA Walnut Gulch Experimental Watershed raingages locations.
Basin area
147 km2

## Slide 28
Storm of 2 August 1957
Raingauge intensities, mm/hr

## Slide 32
Walnut Gulch continues to provide a key focus for a wide range of hydrological studies, including evaporation, sediment transport and remote sensing test applications. see, for example: 50 Years of Research and Data Collection: US Department of Agriculture Walnut Gulch Experimental Watershed. Water Resources Research Vol 44, Issue 5, May 2008
However, the challenges of process understanding and appropriate representation in hydrological models remain:
Spatial variability of precipitation is hard to characterize
Overland flow is a dominant process – but effects of surface processes on infiltration are little studied
Wadi flows are unreliable indicators of upstream flows
Transmission losses are dominant – but complex streambed processes are variable in space and time and poorly understood
Groundwater recharge from ephemeral surface flows is a key water resource, yet is uncertain, depending on complex surface processes and heterogeneous subsurface properties

## Slide 33: Modelling challenges
Michaud and Sorooshian (1994) used the Walnut Gulch dense raingauge network to show that a typical network raingauge density (1 gauge per 20 km2) would lead to significant errors in flow modelling (58% of peak flow). Similarly, using the available 4km radar rainfall product led to 50% errors in peak flows.

## Slide 34: Modelling flood response in Wadi Ahin, Oman (Al-Qurashi et al. 2007)

## Slide 35: Wadi Ahin, Northern Oman (Area 810 km2)
Catchment delineation
Raingauge locations shown in red

## Slide 36: KINEROS process representation
Wadi Ahin - planes and channels

## Slide 37: Modelling approach
Hourly modelling, individual events
27 events, 1996-1999
Physics-based Kineros model
Calibration using 20,000 MC realisations for 5 different objective functions

## Slide 38: Effect of different rainfall interpolation methods

## Slide 39: Alternative performance criteria (objective functions)
Peak discharge
Event volume
Time of peak

## Slide 40
Wadi Ahin
Event of
11 March 1996
Calibration a)-d)
default e)
and ensemble
simulations f)
(best parameter
sets from each
of 28 events)

## Slide 41: Performance for peak flow (OF1) and volume (OF2) for three prediction strategies – (calibration for OF4)

## Slide 42: Regression models for flow peak and volume with observed data and 90% confidence intervals.
R2=0.49
R2=0.60
Regression outperforms the physics-based simulation

## Slide 43: Streamflow Presence and Flood Hazard Detection in Arid Rivers
Zhaocheng Wang
ASU Center for Hydrologic Innovations
Wang, Z., and Vivoni, E.R. 2022. Detecting Streamflow in Dryland Rivers using CubeSats. Geophysical Research Letters. 49(15): e2022GL098729.

## Slide 44: Small Satellites
Planet Labs (http://www.planet.com):
  Commercial, publicly-traded
  Space imaging and data company
  Multisector applications
  Available for scientific purposes via NASA CubeSat program
  Dove Fleet or Constellation:
  >120 CubeSats in low-Earth orbit
  PlanetScope imagery in 4 bands
  Near-daily revisit times
  High resolution (3 to 4 meters)
Planet Labs Dove CubeSats 4 band Imagers

## Slide 45: Small Satellites
Basic Principles of Passive Imaging:
  Solar radiation reflected from surface
  Orbiting camera acquires reflection
  Multiple spectral bands (B, G, R, NIR)
  Bands are differentially sensitive to water, plants, soils, etc.
  Image Acquisition and Processing:
  Radiometric, geometric and atmospheric corrections applied
  Image merging into 25-km scenes
  Resolution of 3-4 meters within scene
Basic Principles from Remote Sensing
25-km
25-km
3-m
3-m

## Slide 46: Hassayampa River River basin, land cover and hydrography

## Slide 47: Streamflow Presence Hovmoller diagram and aggregations in time and space
Daily Flowing Fraction (FFC)
Fraction of Flowing Days (FFD)

## Slide 48: Gila Bend Flooding Hydrography, flood risk and infrastructure
Historical Flood Events in Gila Bend, AZ

## Slide 49: Gila Bend Flooding August 13-14, 2021, fatal flash flood
BW = 102 mm
>300-yr daily
STW @ I8: 396 m3/s
BW: 11 m3/s
  Rim-to-valley mesoscale convective system over central Arizona
  Torrential rains (30 to 100 mm) led to 60-year flood event at Sand Tank Wash
  State of Emergency (2 fatalities, 100 evacuees, >150 damaged buildings)

## Slide 50: Flood Detection NIR difference method applied to flood conditions
August 13-14, 2021
September 19, 2018
Type 1: Water in Channel or Ponded over Surfaces
Type 2: Flood Debris on Urban and Natural Surfaces

## Slide 51: Conclusions - 1
The need for improved science and appropriate training for arid areas has long been recognized. UNESCO’s arid zone water programme (GWADI, https://gwadi.org) was established in 2003, following an Arab Region initiative. GWADI has established successful regional networks, supports Centres of Excellence and maintains a web-site with data products and information.
Despite decades of continued activity, major scientific challenges remain. Scarcity of data is a critical limitation, from routine monitoring networks and the intensive, focussed, multi-disciplinary experimental studies needed to unravel the scientific puzzles that remain. Such studies are resource intensive, may require many years (or decades) of support given the infrequency of major events, and fit poorly with established mechanisms for graduate training.

## Slide 52: Conclusions - 2
This paper has identified some key scientific challenges:
Capturing and modelling spatial rainfall
Understanding infiltration, evaporation and overland flow processes for sparsely vegetated soils
Understanding the dynamic processes of wadi bed infiltration during the passage of floods
Understanding stream-aquifer interactions, including flow emergence
Understanding groundwater recharge processes, including fracture flows in mountain block environments
While remote sensing can play an important role, understanding surface and near surface processes requires dedicated field observation and experimentation

## Slide 53: Conclusions -3
Over the last 20 years, increased computing power has led to new tools and new insights for model application, but for arid areas, their special characteristics, particularly rainfall spatial variability and transmission loss, add considerable complexity and challenge.
Little methodological research has been published; commonly models developed elsewhere are used with limited data and critical assessment of their performance.
The one model that has been designed for these arid areas and quite widely used is the USDA Kineros model.
More experience is needed of the parameter values needed by physics-based hydrological models, their relationship to catchment characteristics, their scale dependence, their uncertainty and associated model sensitivity.
And for conceptual models, there is a need to develop local experience of appropriate parameter values.

## Slide 54: Conclusions - 4
Representation of rainfall is a key issue, in particular the definition of uncertainty in precipitation inputs to hydrological models.
Radar is an exciting possibility to provide spatial rainfall data and is increasingly being deployed for rainfall measurement in arid areas, but high spatial resolution is needed. High resolution atmospheric modelling also offers potential.
Given inevitable data limitations, for long-term simulation rainfall is probably best handled using stochastic models to generate rainfall sequences that represent spatial and temporal variability. However, modern tools have not been tested for arid areas and all methods need detailed data sets for their development and calibration.

## Slide 55: Conclusions - 5
Given the challenges for water management in arid areas, improved science and hydrological modelling are essential.
Much work is still needed to build experience to support model applications in arid areas.
This requires:
dedication to the provision of good quality data
awareness of the potential of new modelling tools
the development of a core of expertise at local and regional level
willingness to share knowledge and experience within and between the world’s arid regions.

## Slide 56: For more information:
See 2 GWADI books:
Wheater, H.S., Sorooshian, S. and Sharma, K.D. (Eds.). 2007 Hydrological modelling for arid and semi-arid areas. Cambridge University Press. 195pp.
Wheater, H.S., Mathias, S. and Li, X. (Eds). 2010. Groundwater modelling in arid and semi-arid areas. Cambridge University Press. 137 pp.
And check out the GWADI
web-site: www.gwadi.org

## Slide 57: Selected papers
Al-Qurashi, A. et al. 2008. Application of the Kineros2 rainfall-runoff model to an arid catchment in Oman. J. Hydrol., 355(1-4): 91-105.
Andersen, N.J. et al. 1998. Sustainable development of alluvial groundwater in sand rivers of Botswana. In: Hydrology in a Changing Environment, Vol. II, Eds. H.S. Wheater and C. Kirby, Wiley, pp367-376.
Farquharson et al. 1992. Regional flood frequency analysis in arid and semi-arid areas. J.Hydrol. 138, 3-4, 487-501
Kenabatho, P. et al. 2012. Stochastic simulation of rainfall in the semi-arid Limpopo basin, Botswana. Int. J. Climatol., 32(7): 1113-1127.
McIntyre, N. et al. 2007. Regression analysis of rainfall-runoff data from an arid catchment in Oman. Hydrolog. Sci. J., 52(6): 1103-1118
McMahon, T.A., (1979) Hydrological characteristics of arid zones. Proc. Symp. Hydrology of Areas of Low Precipitation, Canberra, IAHS Publ. No. 128, pp. 105-123.
Nemec, J. and Rodier, J.A., (1979) Streamflow characteristics in areas of low precipitation. Proc. Symp. Hydrology of Areas of Low Precipitation, Canberra, IAHS Publ. No. 128, pp. 125-140.
Parissopoulos, G.A. and Wheater, H.S. 1991. "Effects of wadi flood hydrograph characteristics on infiltration. J. Hydrol., 126: 247-263.
Parissopoulos, G.A. and Wheater, H.S. 1992. Experimental and numerical infiltration studies in a wadi stream‑bed. J. Hydr. Sci., 37: 27-37.
Parissopoulos, G.A. and Wheater H.S. 1992. Effects of hysteresis on groundwater recharge from ephemeral flows. Water Resour. Res., 28(11): 3055-3061.
Pilgrim, D.H. et al. 1988 Problems of rainfall-runoff modelling in arid and semi-arid regions. Hydrol. Sci. J., 33(4): 379-400.
Wang, Z., and Vivoni, E.R. 2022. Detecting Streamflow in Dryland Rivers using CubeSats. Geophysical Research Letters. 49(15): e2022GL098729.
Wheater, H.S. 1996. Wadi hydrology: process response and management implications. In: Proc UNESCO-NWRC-ACSAD Workshops on Wadi Hydrology and Groundwater Protection. IHP-V Technical Document in Hydrology No 1, UNESCO, Cairo.
Wheater, H.S. and Bell, N.C. 1983. Northern Oman flood study. Proc. Instn. Civ. Engrs., 75: (Part 2), 453‑473. (Awarded ICE Overseas Premium).
Wheater, H.S. et al. 1991. A multivariate spatial‑temporal model of rainfall in S.W. Saudi Arabia. I. Data characteristics and model formulation. J. Hydrol., 125: 175-199.
Wheater, H.S. et al. 2005. Spatial-temporal rainfall modelling for flood risk estimation. Stoch. Environ. Res. Risk Assess., 19(6): 403-416.
Wheater, H.S. et al. 1989. Design rainfall characteristics for SW Saudi Arabia. Proc. Instn. Civ. Engrs. Part 2, 87 Dec. 517‑538.
Wheater, H.S. et al. 1991. A multivariate spatial‑temporal model of rainfall in S.W. Saudi Arabia. II. Regional analysis and model validation. J. Hydrol., 125: 201-220.
Wheater, H.S. et al. 1997. An integrated model of arid zone water resources: evaluation of rainfall-runoff simulation performance. In: Sustainability of Water Resources under Increasing Uncertainty (Proceedings of the Rabat Symposium S1,), IAHS Publ. No. 240, pp 395-405.
50 Years of Research and Data Collection: US Department of Agriculture Walnut Gulch Experimental Watershed. Water Resources Research special section Vol 44, Issue 5, May 2008

## Slide 58: Atacama desert headwaters, Chile Transboundary water management

## Slide 60: Observational and modelling studies are published in a Special Issue of WiresWater (2023/2024), e.g.:
Understanding the Silala River – scientific insights from the dispute over the status and use of the waters of the Silala (Chile v. Bolivia) DOI: 10/1002/wat2.1663
Investigating the effects of channelization in the Silala River: A review of the implementation of a coupled MIKE-11 and MIKE-SHE modelling system DOI: 10/1002/wat2.1673
Introduction to the Silala River and its Hydrology DOI: 10/1002/wat2.1644
The development of a hydrogeological conceptual model of groundwater and surface water flows in the Silala River Basin DOI: 10/1002/wat2.1676
Groundwater modelling of the Silala basin and impacts of channelization DOI: 10/1002/wat2.1662
Evaporation processes in the Silala River basin DOI: 10/1002/wat2.1638
The Quebrada Negra wetland study….. DOI: 10/1002/wat2.1683
Investigating river-aquifer interactions using heat as a tracer in the Silala river transboundary basin DOI: 10/1002/wat2.1639
Hydrochemical and isotopic evaluation of groundwater and river water in the transboundary Silala River watershed DOI: 10/1002/wat2.1679

## Slide 61: Sand rivers of Botswana

## Slide 62: Proposed Yucca Mountain Nuclear Waste Repository
Source US Department of Energy
Office of Civilian Radioactive Waste Management
Yucca Mountain Repository License Application
June 2008

## Slide 63: Proposed Yucca Mountain Nuclear Waste Repository
Source US Department of Energy Office of Civilian Radioactive Waste Management Yucca Mountain Repository License Application June 2008

## Slide 64
2. Case Study -
Recharge
Management,
Wadi Ghulaji,
Sultanate of Oman
Basin area 758 km2

## Slide 65
Falaj system

## Slide 66
Recharge Dam – Batinah coastal plain,
Oman

## Slide 67
Wadi Ghulaji geology

## Slide 70
Model performance
- a single observed event